## Slide 1: Investigating Transport and Structural Changes of Faults Slipping under sc-CO2 Conditions in Shale
Nov 9th, 2021
Talal Al Shafloot1, Arjun Kohli1, Tae Wook Kim1, Anthony Kovscek1
1 Energy Resources Engineering Department, Stanford University

## Slide 2: Problem
Modified after Fang et al., (2017)
(Al Shafloot et al., 2020)
sc-CO2
water
- Permeability evolution?
- Effect of slip on diffusion?
- sc-CO2 adsorption effect?
- sc-CO2 diffusion?
Notes: sc-CO2 stimulation agent, enhances productivity by: tensile fracturs or triggering pre-existing faults.
We investigated performance compared to water, utilized imaging techineques.
Triggering pre-existing, several questions with no clear answers.

## Slide 3: Background
  Effect of slippage on permeability:
    Gouge with water (Okazaki et al., 2013; Takahashi et al., 2007)
    Saw-cut and natural fault with Argon (Wu et al., 2017)
  Fracture/fault measuring permeability methods:
    Pulse decay (Kumar et al., 2015)
    Steady-state (Cai et al., 2014)
    Pore pressure oscillation (Takahashi et al., 2007)
  Utilizing X-ray CT for permeability investigation:
    Fracture evolution of Coal samples (Cai et al., 2014)
(Cai et al., 2014)
(Okazake et al., 2013)
(Wu et al., 2017)
Notes: -Okazaki, K., Katayama, I., & Noda, H. (2013). Shear‐induced permeability anisotropy of simulated serpentinite gouge produced by triaxial deformation experiments. Geophysical research letters, 40(7), 1290-1294.
-Takahashi, M., Mizoguchi, K., Kitamura, K., & Masuda, K. (2007). Effects of clay content on the frictional strength and fluid transport property of faults. Journal of Geophysical Research: Solid Earth, 112(B8).
-Wu, W., Reece, J. S., Gensterblum, Y., & Zoback, M. D. (2017). Permeability evolution of slowly slipping faults in shale reservoirs. Geophysical Research Letters, 44(22), 11-368.
-Kumar, H., Elsworth, D., Mathews, J. P., & Marone, C. (2016). Permeability evolution in sorbing media: analogies between organic‐rich shale and coal. Geofluids, 16(1), 43-55.
-Cai, Y., Liu, D., Mathews, J. P., Pan, Z., Elsworth, D., Yao, Y., ... & Guo, X. (2014). Permeability evolution in fractured coal—combining triaxial confinement with X-ray computed tomography, acoustic emission and ultrasonic techniques. International Journal of Coal Geology, 122, 91-104: investigated using microCT and fracture evolution of coal samples as a result of cyclic loading.

## Slide 4: Goals
  Motivation
    Understand spatial and time scales of sc-CO2 diffusion from active faults
    Study effects of matrix composition and anisotropy
    Study effects of fault slip and matrix damage on permeability
  Objectives:
    Visualize dynamics of diffusion in low permeability, layered media
    Quantify permeability of fault plane before/after/during slip
    Quantify impact of fault slip and damage on diffusivity
Notes: Goals of trial tests:
Determining optimum experimental plan to accomplish goals.
Investigating possible imaging issues and confirming applicability.
Investigating feasibility to capturing diffusion dynamics across faults.
Determining suitable timing for experimental steps.

## Slide 5: Experimental Work
  Sample information
 | Sample name | Formation
Test 1 | Z-2-6-V | Wolfcamp shale
Test 2 | Z-6-2-V | 0.978
Test 2
Test 1
Step | Objectives
µ-CT scanning (before and after) | Observe structural changes
Inject Kr | Quantify porosity Monitor diffusion
Inject CO2 | Visualize Storage Capacity
Induce incremental slip | Quantify friction coefficient
Continue CO2 injection | Investigate storage capacity increase
* Permeability is measured at different stages to monitor evolution
  Sample preparation
  Experimental workflow

## Slide 6: Experimental Setup
(Glatz et al., 2018)
Notes: Talk about leakage and point it out
TALK ABOUT BOTH P AND T, THAT’S AN ADVANTAGE FOR YOUR WORK TO KEEP THE T AND P BOTH SIMILAR TO RESERVOIR CONDITION
CT scan of the main cell

## Slide 7: Results: Fault Slip
  Resolved shear and normal stresses:
  Summary
Test | Objective | Vertical displacement (mm)
1 | Pore pressure induced slip | 2.5
2 | Incremental axial load induced slip | 2.2
Notes: Plots of n and B vs differential stress

## Slide 8: Results: Fault Slip
  Pore pressure induced (test 1):
    Fault slipped at µ = 0.57
    Identified maximum vertical displacement
1300psi pore pressure applied
  Axial loading induced (test 2):
    Five slipping intervals
    Fault slipped at µ = 0.61
    Similar trend to work in literature

## Slide 9: Results: Permeability Evolution
  Steady state (Rutter et. al., 2018)
  Transmissivity (kt) has the dimension of M3
(a) Coordinate system for electric dipole (b) Nonconductive elliptical boundary to a conductive surface (Rutter et. al., 2018)
(a) Coordinate system)
Notes: -flow of viscous fluid through a permeable matrix or through a more conductive crack are respectively analogous to the flow of electric current through a resistive solid or thorough a thin resistive sheet embedded within an insulating medium.
-not necessary to know the crack thickness.
-cmpare fluid transport capacity of the crack with that of flow through a matrics permeability km, given that permability is in effect the transmissivity of a meter thick layer of matrix material.

## Slide 10: Results: Permeability Evolution
  Saturation effect (test 1):
    Saturating with Kr and CO2 reduced fracture permeability by 52%
    Vacuuming did not change permeability values: permeant damage

## Slide 11: Results: Permeability Evolution
  Slip effect (test 2):
    Saturating with CO2 reduced fracture permeability by 25%
    Fault slippage further reduced permeability by an additional 29%
    Relaxation after slip reduced permeability by an additional 8%

## Slide 12: Results: Validating Steady-state
  Flow inside borehole (test 2):
    Maximum Re = 360
    Laminar: Re < Rec = 2000
  Flow along fracture (test 2):
    Re ranges from 20.5 to 47.9
    Rec in literature: 1 to 20
  Large Re for fracture flow is acceptable:
    Linear behavior for ∆p vs Q
    Rec in literature increases as fracture is smoother
1
2
Javadi et. al., 2014
Test 2: beginning of the injection (left) post slip (right)

## Slide 13: Results: Dynamic CT Imaging of Kr-filled Porosity
  Saturating with Kr (test 2):
    Porosity distribution helps visualizing diffusion
    Visualization confirms diffusion around fault vicinity
car
car
car
borehole
2.5 hrs
52 hrs
64 hrs

## Slide 14: Results: Dynamic CT Imaging of Kr-filled Porosity
  Saturating with Kr (test 2):
    Wolfcamp samples have small porosity
    Longer saturation time is needed

## Slide 15: Summary
  Faults were successfully slipped with both pore pressure and incremental axial loading. Estimation of jacketing resistance is needed to quantify µ.
  Steady-state approach was utilized and validated to measure fracture permeability.
  Saturating with fluids with large adsorption capacity reduces permeability. Saturating with sc-CO2 decreased fracture permeability by at least 25%.
  Slipping a smooth fault considerably reduced fault permeability.
  CT Imaging helped visualizing diffusion of fluids and quantifying porosity.

## Slide 16: Acknowledgment
  King Fahd University of Petroleum and Minerals (KFUPM)
  Saudi Arabian Cultural Mission (SACM)
  Natural Gas Initiative (NGI)
  Stanford Center for Carbon Storage (SCCS)
  This work was supported as part of the Center for Mechanistic Control of Unconventional Formations (CMC-UF), an Energy Frontier Research Center funded by the U.S. Department of Energy, Office of Science under DOE (BES) Award DE-SC0019165

## Slide 17
            Thank You!